## Slide 1
RESEARCH · BUILD · DEMO
Window Agent & Roof Plan Agent
Deterministic, constraints-first daylight compliance · lighting-aware roofing
shift-left · provable · IRC-grounded
Ojas · AI Gurukul · PS-II

## Slide 2
OVERVIEW
Two agents
Window Agent
Turned Aadi's daylight *scorer* into a
shift-left, deterministic *constraint* layer.
Hard code rules (egress, light, glazing) are
given to the generator + proved by Z3;
the soft daylight score stays non-blocking.
Roof Plan Agent
Deterministic roof geometry (gable/hip/shed/
flat), multi-floor stepped roofs, pitch +
drainage — Z3-self-verified. Now places
sunroofs using the Window Agent's daylight
scores (lighting-aware roofing).
Both are pure, reproducible, no-LLM tools that plug into the Z3 Verifier + DXF/PDF exports.
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
2

## Slide 3
WINDOW AGENT
The starting point, and the feedback
What existed
A deterministic daylight SCORER + suggester:
ranks exterior walls by sun exposure + tree
shade, suggests windows to hit a window-to-
floor ratio, scores daylight 0–100.
No LLM · reproducible · a soft signal.
The gap: it verifies AFTER the fact and enforces no hard code rules (egress, glazing, sill).
feedback
Follow the LAC guideline
Lighting-only verification adds latency (retry loops)
Shift-left: give lighting as constraints, not post-checks
Explore deterministic vs non-deterministic verification
Formalise the hard window rules (egress, tempered glass,
sill/header, per-room placement) with Constraint Engine
+ Floor Plan
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
3

## Slide 4
THE LAC GUIDELINE
Latency · Accuracy · Concurrency → three decisions
"LAC" is a systems trilemma. It isn't a separate task — it is the rationale for every decision below.
L
Latency
Don't stall in retry loops
Decision 2 — SHIFT-LEFT the hard rules into constraints, so illegal windows aren't generated → far fewer generate→verify→fail rounds.
A
Accuracy
Verdicts correct & reproducible
Decision 1 — DETERMINISTIC verification: a provable, same-input→same-verdict gate (a stochastic sim can't guarantee this).
C
Concurrency
Agents run in parallel
Decision 2 (soft tier) — the daylight SCORE is NON-BLOCKING; Livability runs concurrently, only a real violation gates.
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
4

## Slide 5
DECISION 1 — ACCURACY
Lighting/compliance verification is DETERMINISTIC
cols: Approach
Approach
Reproducible
Provable
Latency
A
Deterministic analytic (WWR, sun-weight, code predicates)
Yes
Yes
~ms
B
Physically-based daylight sim (Radiance, Monte-Carlo)
No*
No
sec–min
C
LLM / ML judge of "is the lighting ok"
No
No
slow + $
The linchpin: shift-left requires determinism — you can only hand a rule to the generator as a CONSTRAINT if it is a decidable predicate. A Monte-Carlo daylight score can never be a constraint, only a post-hoc score.
* Monte-Carlo daylight metrics vary run-to-run — unacceptable for a legal gate.
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
5

## Slide 6
DECISION 2 — LATENCY
Shift-left: split HARD constraints from the SOFT score
Before — verify after the fact
generate
verify
FAIL
regenerate
↺ every failed round is a full (LLM) regeneration = latency
After — constraints first (correct-by-construction)
constraints given up front
generator satisfies them
verify (usually passes)
HARD (gate): egress · light ≥8% · vent ≥4% · safety glazing · sill — proved by Z3, given to the generator.
SOFT (score): daylight quality, orientation, tree-shade, aesthetics — Aadi's agent, non-blocking, in the report.
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
6

## Slide 7
DECISION 3 — THE RULE SET
Every hard rule grounded in the IRC (auditable, city-tunable)
egress_window
Each sleeping room: 1 operable window, net clear ≥ 5.7 sq ft, ≥ 24 in H, ≥ 20 in W, sill ≤ 44 in
IRC R310
natural_light
Habitable room glazing ≥ 8% of floor area
IRC R303.1
natural_ventilation
Openable area ≥ 4% of floor area
IRC R303.1
safety_glazing
Sill < 18 in, wet rooms, or next to a door → must be tempered
IRC R308.4
operable-for-egress
Egress windows must be an operable type (fixed/picture rejected)
IRC R310
(city) values — the tempered-sill and egress-sill thresholds — are overridable per jurisdiction by the Constraint Engine ruleset.
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
7

## Slide 8
FEEDBACK → RESPONSE (1/3)
The four principles
Q1
Follow the LAC guideline
→ Identified LAC = Latency·Accuracy·Concurrency; the three design decisions each target one leg.
Q2
Lighting-only verification adds latency
→ Confirmed — the generate→verify→fail loop is the cost; addressed by shift-left.
Q3
Shift-left lighting as constraints
→ Built verify_windows: hard rules are now constraints given to the generator + proved, not post-hoc checks.
Q4
Deterministic vs non-deterministic?
→ Decided DETERMINISTIC, with the linchpin justification (shift-left needs decidable predicates).
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
8

## Slide 9
FEEDBACK → RESPONSE (2/3)
The window rules made HARD + provable
✓
Bedrooms need fire-escape windows
egress_window — IRC R310 (≥5.7 sqft, 24×20 in, sill ≤44 in, operable)
✓
Tempered glass below height X
safety_glazing — IRC R308.4, city-tunable sill threshold
✓
Sill / header height
sill_height_ft field; enforced by egress + tempered rules
✓
Enough light & air per room
natural_light ≥8%, natural_ventilation ≥4% — IRC R303.1
✓
Fire-egress ⇒ operable (sliding/openable)
egress requires an operable window type
All deterministic, city-parameterisable, and callable as verify_windows(windows, rooms, constraints=ruleset).
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
9

## Slide 10
FEEDBACK → RESPONSE (3/3)
Placement & aesthetics — soft, or needs coordination
Bathroom window near shower / 3×2 max
SOFT — needs fixture (shower) position from Floor Plan
Master bath windows around the tub
SOFT — needs tub position from Floor Plan
Walk-in closet: small, high window
SOFT — placement heuristic
Kitchen window above the sink
SOFT — needs sink position from Floor Plan
Bedroom window not behind the bed
SOFT — needs bed position from Floor Plan
Aesthetic glazing scales with budget
SOFT — a Livability score dimension, not code
Garage window; patio ⇒ sliding door
Optional / handled by Floor Plan (doors)
Decision: promote these to HARD checks the moment the Floor Plan agent emits fixture coordinates (sink, bed, tub). Coordination item with Prasad.
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
10

## Slide 11
WINDOW AGENT — DEMO
Deterministic, ~6 ms, exact measured-vs-required
$ verify_windows(compliant)
3 rooms: bedroom, living, bathroom
ok : True
n_failed : 0
solve_time_s : 0.006
# egress, light, vent, safety
# glazing all satisfied
$ verify_windows(non_compliant)
ok : False n_failed : 6
✗ egress_window bed (R310)
✗ natural_light 4<12 bed (R303)
✗ natural_ventilation 0<6 bed
✗ natural_light 4<24 living(R303)
✗ natural_ventilation 4<12 living
✗ safety_glazing sill 12in<18in
Every violation carries the measured value, the required value, and the IRC section — ready to feed a generator retry or a reviewer.
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
11

## Slide 12
RESEARCH CONTRIBUTION
Constraints-first residential daylight compliance
Prevailing: generate-then-simulate
An LLM / diffusion model proposes; a physically-based simulator scores the daylight afterwards. Stochastic, slow, can't constrain generation.
Ours: a dual-use predicate
The SAME deterministic, IRC-grounded predicate both constrains generation (correct-by-construction) AND proves compliance. Only possible because it's deterministic.
The claim: separate "is it legal" (provable) from "is it nice" (scored) — and reuse the legal predicate as a generator constraint. A clean paper angle in generative building design.
Grounding: IRC R310 (egress) · R303.1 (light/vent) · R308.4 (safety glazing) · full memo: WINDOW_AGENT_RESEARCH.md

## Slide 13
ROOF PLAN AGENT
Deterministic geometry · Z3-self-verified · Cluster 4
Input ← Elevation / Multi-floor (+ Window daylight)
Output → roof polygons "view_type":"roof" → DXF Generator + PDF
Generates: roof outline (matches footprint exactly), ridge, hips, per-plane pitch + drainage, heights.
Roof types
gable
hip
shed (mono-pitch)
flat (drained)
+ multi-floor STEPPED roofs (a lower shed over the garage), per-level roof types.
Self-verifies before handoff (same propose→prove pattern as the generators)
roof_matches_footprint
stepped_roof_downward
roof_eave_setback
pitch_specified
drainage_specified
skylight_within_roof
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
13

## Slide 14
ROOF DEMO + LIGHTING INTEGRATION
Sunroof placed from the Window Agent's daylight scores
The skylight rule
Reads per-room daylight scores from the
Window Agent → drops a sunroof over each
UNDER-LIT top-floor room (score < 45), on
its sunniest roof plane (prefers S/E/W).
ROOF PLAN — VERIFIED ✓
main gable 5:12 ridge 28.8ft
garage shed 5:12 (stepped, lower)
sunroof → family_room (score 34)
on the E (sun) plane
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
14

## Slide 15
HOW IT CONNECTS · STATUS
Two agents, one daylight-aware pipeline
Window Agent
daylight scores +
hard constraints
Roof Plan Agent
sunroof placement +
roof geometry
Z3 Verifier
provable
compliance
DXF / PDF
permit
artifacts
DONE
Window constraint layer (egress/light/vent/glazing), deterministic + IRC-cited
Roof agent: geometry, stepped roofs, pitch/drainage, DXF+SVG
Skylight placement from daylight scores
All Z3-self-verified; demos + docs written
NEXT (coordination)
Constraint Engine (Harshit): add a windows block + per-city thresholds
Floor Plan (Prasad): emit fixture positions → promotes SOFT placement to HARD
Confirm Aadi's exact daylight-score field name
Optional: physically-based sim as an offline quality enrichment
Window Agent + Roof Plan Agent · Ojas · AI Gurukul PS-II
15